## Slide 1
Knowledge sharing
  gstreamer
Thao luong
February 28, 2017
Gstreamer prj., multimedia fw team
R-Car Software Solution 2 group
Renesas design vietnam co., ltd.

## Slide 2: Agenda
GStreamer and RVC Gstreamer project 3
Knowledge for user of GStreamer 15
Knowledge for developer of GStreamer 19
Q & A 34

## Slide 3
Project overview
Piture got from: https://twitter.com/gstreamer

## Slide 4: Project overview
GStreamer Framework (v.1.6.3)
v4l2src
gst-omx
vspfilter
waylandsink
alsasink
Video Capture driver
OMX
Video
OMX
Audio
vsp2driver
Wayland/
Weston
Alsa
Target of dev.
Target of test
RCarGen3
H264 (enc/dec)
H265 (dec)
MPEG4 (dec)
VC1 (dec)
VP8 (dec)
AAC (dec)
MP3 (dec)
WMA (dec)
Full HD/60fps
Full HD/60fps
We support audio & video playback, capture and encode on RCarGen3 platform using GStreamer framework

## Slide 5: RVC gstreamer project
In-charge of:
  Development of v4l2src (capture plugin) which use Renesas BSP
  Development gst-omx (audio/video decode & video encode plugins) which use Renesas OMX IL library
  Ensure v4l2src and all supported elements of gst-omx can run without error on RCarGen3
  Verify GStreamer framework on RCarGen3

## Slide 6: RVC gstreamer project
GStreamer framework have 5 main packages and some other packages like gst-omx or gstlibav
    GStreamer: the core package
    gst-plugins-base: an essential exemplary set of elements
    gst-plugins-good: a set of good-quality plug-ins under LGPL
    gst-plugins-ugly: a set of good-quality plug-ins that might pose distribution problems
    gst-plugins-bad: a set of plug-ins that need more quality
  We only care for gst-omx and gst-plugins-good

## Slide 7
Knowledge for user of GStreamer

## Slide 8: Knowledge for user of GStreamer
What is knowledge which user of GStreamer need to know?
  What is GStreamer?
  Basic concepts of GStreamer
  How to create pipeline using gst-launch tool
  How to build GStreamer in yocto
  How to Install built packages into filesystem

## Slide 9: What is gstreamer ?
Is a framework for creating streaming media applications
The fundamental design comes from the video pipeline at Oregon Graduate Institute, as well as some ideas from DirectShow
Possible to write any type of streaming multimedia application
Advantage:
The pluggable components can be mixed and matched into arbitrary pipelines. This pipeline defines the flow of the data

## Slide 10: Gstreamer framework
Picture got from: https://gstreamer.freedesktop.org/documentation/application-development/introduction/gstreamer.html
Applications and tools
GStreamer core provided gst-inspect to query information of plugins; gst-launch to create pipeline from elements of plugins
Core:
Provide framework for plugins, data flow and media type handling/negotiation
Provide API for application
Plugins:
There are many types of plugins, basic plugins and plugins from 3rd party
Plugins and their elements can be found at: https://gstreamer.freedesktop.org/documentation/plugins.html

## Slide 11: Basic conceps of gstreamer
Elements
On GStreamer, each element has one specific function, for example, read data from file, decode, encode and so on.
Element linked together and let data go through them
Chaining several element together, a pipeline for a specific task is created.
Input and out put of element are called pads.
  Sink pad is input of element, where receive data from other element
  Source pad is output element, where send data to other element
Element
Sink
Source
Data
Data

## Slide 12: Basic conceps of gstreamer
The element type can be classified depend on number of pads:
Element
Sink
Data
Data
Element
Source
Data
Source elements: only have source pad
Element
Sink
Source
Data
Filter and filter-like elements:
have both source and sink pad
Sink elements: only have sink pad

## Slide 13: Basic conceps of gstreamer
Capabilities of pads (caps)
  Describe the type of data that is streamed between two pads, or that one pad (template) supports
  Example of caps of sink pad and src pad of one audio decoder:
  Can get information of caps via gst-inspect and it will show as information of next page
Element
Sink
Source

## Slide 14: Basic conceps of gstreamer
Capabilities of pad (caps)
Direction of pads: source pad
Direction of pads: sink pad
Caps of source pad
Caps of sink pad

## Slide 15: Basic conceps of gstreamer
Caps negotiation
  Capabilities of 2 pads are compatible each other
  Ex:
Negotiate
h264parse
Sink
Source
video/x-h264
parsed: true
stream-format: { avc, avc3, byte-stream }
alignment: { au, nal }
omxh264dec
Sink
Source
video/x-h264
alignment: au
stream-format: byte-stream
width: [ 1, 2147483647 ]
height: [ 1, 2147483647 ]
video/x-raw
format: { NV12, I420 }
width: [ 1, 2147483647 ]
height: [ 1, 2147483647 ]
Caps negotiation

## Slide 16: How to create pipeline
Pipeline can be created by using gst-launch tool to connect for elements on system:
  Elements will connect each other by “!”. Element before “!”, we call upstream element. Element after “!”, we call downstream element.
  Elements on pipeline will decide for data flow.
  Ex: Pipeline decode, convert and show video on screen:
  # gst-launch-1.0 filesrc location=file.mp4 ! qtdemux ! h264parse ! omxh264dec ! vspfilter ! waylandsink
NV12
vspfilter
File.mp4
FileSystem
(NFS)
filesrc
h264parse
omxh264dec
waylandsink
qtdemux
BGRA
element
Sink pad
Src pad

## Slide 17: How to create pipeline
Besides, we can assign type for negotiation by using capsfilter element in case element have many types.
Ex: omxh264dec can sent data with format is NV12 and I420, normally it will use NV12 as default for caps negotiation with other element.
But we can choose I420 to make negotiation:
# gst-launch-1.0 filesrc location=file.264 ! h264parse ! omxh264dec ! capsfilter caps=video/x-raw,format=I420 ! vspfilter ! waylandsink
shorten pipeline:
# gst-launch-1.0 filesrc location=file.264 ! h264parse ! omxh264dec ! video/x-raw,format=I420 ! vspfilter ! waylandsink
vspfilter
File.264
FileSystem
(NFS)
filesrc
h264parse
omxh264dec
waylandsink
I420
BGRA

## Slide 18: How to create pipeline
So to create pipeline for audio and video, you should have basic knowledge about audio and video, such as:
  Container (Mp4, mv4, …), codec (H264, H265, VC1, AAC, MP3, …), video format (NV12, NV16, BGRA, …)
Base on these information, we will choose a suitable demuxer, parser and decoders corresponding to video stream (please refer to Appendix for example)
Can specify supported elements on system by gst-inspect tool:

## Slide 19: How to create pipeline
In case you don’t have knowledge about the video file, can use playbin:
  # gst-launch-1.0 -v playbin uri=file:///path/to/somefile.mp4
Playbin will detect suitable elements in filesystem for playback automatically.
For more information, can refer to: https://gstreamer.freedesktop.org/data/doc/gstreamer/head/gst-plugins-base-plugins/html/gst-plugins-base-plugins-playbin.html

## Slide 20: How to build gst in yocto
Normally, GStreamer will be built with yocto in case BSP + 3D Graphics + Multimedia package. Please refer to 3.1 RENESAS_RCH3M3_YoctoStartupGuide_UME_vx.xx.x.pdf
But we can rebuilt packages of GStreamer by following command line:
  #bitbake gstreamer1.0xxx –C configure
  (Please refer to yocto team for more knowledge about building)
After building, libraries and configure installed in filesystem will locate at:
$build/tmp/work/aarch64-poky-linux/gstreamer1.0xxx/<version>/image/
gstreamer1.0xxx: gstreamer1.0
gstreamer1.0-plugins-base
gstreamer1.0-omx
…

## Slide 21: How to Install built packages into filesystem
Besides libraries at $build/tmp/work/aarch64-poky-linux/gstreamer1.0xxx/<version>/image/, there are some plugins were built but they didn’t install into filesystem.
Can find them on $build/tmp/work/aarch64-poky-linux/gstreamer1.0xxx/<version>/deploy-ipks/aarch64/
To install for these plugins use “opkg install” plugin.ipk
  Ex: To install for ivfparse element, go to https://gstreamer.freedesktop.org/documentation/plugins.html to check which plugin and module (package) that ivfparse element belongs to. In this case, ivfparse element belongs to gst-plugins-bad package and ivfparse plugin.
  Step1: Go to $build/tmp/work/aarch64-poky-linux/gstreamer1.0-plugins-bad/1.6.3-r0/deploy-ipks/aarch64
  Step2: Copy gstreamer1.0-plugins-bad-ivfparse_1.6.3-r0_aarch64.ipk into filesystem
  Step 3: Install it into filesystem by:
  # opkg install gstreamer1.0-plugins-bad-ivfparse_1.6.3-r0_aarch64.ipk

## Slide 22: Install built packages into filesystem

## Slide 23
Knowledge for developer of GStreamer

## Slide 24: Knowledge for developer of GStreamer
Writing a new plugin is not easy, this document only share knowledge for reading source code of existence plugins and how to debug
First, there are some knowledge which developer of GStreamer need to know:
  Basic understanding of C language (please self study)
  Some knowledge about GObject (you will be OK if you have knowledge of object-oriented and C language. For further study, please refer to http://library.gnome.org/devel/gobject/stable/
  Basic concepts of GStreamer
  Important points when reading source code of GStreamer
  How to debug

## Slide 25: Basic concepts of GStreamer
Elements and Plugins
  Elements:
    At the core of GStreamer. An element is an object derived from the GstElement class
    Elements provide some sort of functionality when linked with other elements.
    Filter element: processes a stream of data
    Source and sink element: producers and consumers of data
    After being created, an element will not actually perform any actions yet. It is necessary to change state to make it do something
source
src
filter
src
sink
sink
sink
Data
Data

## Slide 26: Basic concepts of GStreamer
Elements and Plugins
  Elements:
    Change state in Upward:
NULL
READY
PLAYING
PAUSE
NULL (default state)
No resources are allocated
Transitioning to it will free all resources
PLAYING
The stream is actively processing
(Same as PAUSE with a running clock)
READY
Allocated global resources
But the stream is not opened, the stream positions is automatically zero
PAUSE
Opened the stream, but is not actively processing it.
Allowed to modify a stream's position, read and process data but it is not allowed to play the data (without a running clock)
+ Use gst_element_set_state () to change state for element
+ Element class will be in-charge for change state.
+ In case setting an element from NULL to PLAYING, element will internally change to READY -> PAUSE before PLAYING

## Slide 27: Basic concepts of GStreamer
Elements and Plugins
  Elements:
    Change state in Downward:
NULL
READY
PLAYING
PAUSE
NULL (default state)
No resources are allocated
Transitioning to it will free all resources
PLAYING
The stream is actively processing
(Same as PAUSE with a running clock)
READY
Allocated global resources
But the stream is not opened, the stream positions is automatically zero
PAUSE
Opened the stream, but is not actively processing it.
Allowed to modify a stream's position, read and process data but it is not allowed to play the data (without a running clock)
+ Use gst_element_set_state () to change state for element
+ Element class will be in-charge for change state.
+ In case setting an element from PLAYING to NULL, element will internally change to PAUSE -> READY before NULL

## Slide 28: Basic concepts of GStreamer
Elements and Plugins
  Elements:
    Bin elements: contain other elements. There are 2 types:
        responsible for synchronization of the elements that they contain so that data flows smoothly
        automatically add other elements to the bin and links them together
  Can refer to https://gstreamer.freedesktop.org/data/doc/gstreamer/head/gstreamer/html/GstElement.html or $build/tmp/work/aarch64-poky-linux/gstreamer1.0/1.6.3-r0/gstreamer-1.6.3/gst/gstelement.c
Bin
Element 1
src
Element 2
src
sink
Element 3
sink
Data
Data

## Slide 29: Basic concepts of GStreamer
Elements and Plugins
  Plugins:
    A plugin is essentially a loadable block of code (shared object file or a dynamically linked library)
    A single plugin may contain the implementation of several elements, or just a single one
    The plugin mechanism is used everywhere in GStreamer
  Can refer to https://gstreamer.freedesktop.org/data/doc/gstreamer/head/gstreamer/html/GstPlugin.html or $build/tmp/work/aarch64-poky-linux/gstreamer1.0/1.6.3-r0/gstreamer-1.6.3/gst/gstplugin.c

## Slide 30: Basic concepts of GStreamer
Pads
  Pads are used to negotiate links and data flow between elements in GStreamer
  Pads have specific data handling capabilities: A pad can restrict the type of data that flows through it. Links are only allowed between two pads when the allowed data types of the two pads are compatible
  All data in GStreamer flows one way through a link between elements
  Data flows out of one element through one or more source pads, and elements accept incoming data through one or more sink pads
  Can refer to https://gstreamer.freedesktop.org/data/doc/gstreamer/head/gstreamer/html/GstPad.html or $build/tmp/work/aarch64-poky-linux/gstreamer1.0/1.6.3-r0/gstreamer-1.6.3/gst/gstpad.c
Data
Element
Source
Data
Element
Sink
Source

## Slide 31: Basic concepts of GStreamer
Communication on GStreamer

## Slide 32: Basic concepts of GStreamer
Communication on GStreamer
  buffers are objects for passing streaming data between elements in the pipeline. Buffers always travel from sources to sinks
  events are objects sent between elements or from the application to elements. Events can travel upstream and downstream.
  messages are objects posted by elements on the pipeline's message bus, where they will be held for collection by the application. Messages are used to transmit information such as errors, tags, state changes, buffering state, redirects etc. from elements to the application in a thread-safe way.
  queries allow applications to request information such as duration or current playback position from the pipeline. Queries are always answered synchronously. Elements can also use queries to request information from their peer elements

## Slide 33: Basic concepts of GStreamer
GstMiniObject, Buffers and Events
GstMiniObject
GstBuffer
GstEvent

## Slide 34: Basic concepts of GStreamer
GstMiniObject, Buffers and Events
  GstMiniObject
    is the structure used to hold chunks of data (all streams of data in GStreamer)
    contains:
      An exact type indicating what type of data (event, buffer, ...)
      A reference count (refcount) indicating the number of elements currently holding this miniobject.
      When the reference count falls to zero, the miniobject will be disposed, and its memory will be freed
  Can refer to https://gstreamer.freedesktop.org/data/doc/gstreamer/head/gstreamer/html/gstreamer-GstMiniObject.html or $build/tmp/work/aarch64-poky-linux/gstreamer1.0/1.6.3-r0/gstreamer-1.6.3/gst/gstminiobject.c

## Slide 35: Basic concepts of GStreamer
GstMiniObject, Buffers and Events
  Buffers
    contains a chunk of audio or video data that flows from one element to another
    contain metadata describing the buffer's contents include:
      Pointers to one or more GstMemory objects.
      A timestamp indicating the preferred display timestamp of the content in the buffer.
  Can refer to https://gstreamer.freedesktop.org/data/doc/gstreamer/head/gstreamer/html/GstBuffer.html or $build/tmp/work/aarch64-poky-linux/gstreamer1.0/1.6.3-r0/gstreamer-1.6.3/gst/gstbuffer.c

## Slide 36: Basic concepts of GStreamer
GstMiniObject, Buffers and Events
  Events
    contain information on the state of the stream flowing between the two linked pads
    Events are used to indicate: a media type, the end of a media stream, seeking and so on.
    Event can contain:
      A subtype indicating the type of the event.
      The other contents of the event depend on the specific event type.
  Can refer to https://developer.gnome.org/gstreamer/stable/gstreamer-GstEvent.html or $build/tmp/work/aarch64-poky-linux/gstreamer1.0/1.6.3-r0/gstreamer-1.6.3/gst/gstevent.c

## Slide 37: Basic concepts of GStreamer
Buffer allocation
  Can contains memory allocated by malloc()
  Elements create buffers that point to special memory. Can create via GstBufferPool or GstAllocator. Elements can ask a GstBufferPool or GstAllocator from the downstream. If downstream is able to provide these objects, upstream can use them to allocate buffers

## Slide 38: Important points when reading source code of GStreamer
  When reading source code of a element on GStreamer, to understand it we should care:
    Parent class of element
    Methods of element and initialization value
    Data processing flow

## Slide 39: Important points when reading source code of GStreamer
  Parent class of element
    How to detect?: it is the first field in struct of element/plugin
  Ex: gstomxh264dec
  struct _GstOMXH264Dec
  {
  GstOMXVideoDec parent;
  };
  struct _GstOMXVideoDec
  {
  GstVideoDecoder parent;
  …
  }
gstomxvideodec is parent class of gstomxh264dec
gstvideodecoder is parent class of
gstomxvideodec
Continue this identifying, we will have inheritance:
gstelement
gstvideodecoder
gstomxvideodec
gstomxh264dec
gstobject

## Slide 40: Important points when reading source code of GStreamer
  Parent class of element
    Purpose: Trace for source code and understand operation flow
    For example, source code of gstomxh264dec.c only have some functions and it does not show a completely operation flow, it only handle for format. It doesn’t show how is data handled.
    To understand how is data handled, we must trace on source code of gstomxvideodec.c:
    input data will be handled in gst_omx_video_dec_handle_frame ()
    output data is handle in gst_omx_video_dec_loop ()
gstelement
gstvideodecoder
gstomxvideodec
gstomxh264dec
gstobject

## Slide 41: Important points when reading source code of GStreamer
  Methods of element and initialization value
    Methods is defined on Xxx_class_init() and _class structure (defined on header (.h))
      In class_init() we can specify which methods of parent class will be overridden by element
      And it also defines methods for itself
    Initialization value is defined on Xxx_init():
      initialize object’s instances
    (Xxx will be named base on name of file.)
    Ex: gstomxh264dec.c
    gst_omx_h264_dec_class_init() and gst_omx_h264_dec_init ()
    _class_init() will be loaded before _init()

## Slide 42: Important points when reading source code of GStreamer
  Data processing flow
    On GStreamer, the chain function (_chain ()) is the function in which all data processing takes place
    If there is no _chain() function on element source code, it is implemented on parent class of element.
    Can investigate from this function to understand data processing flow.
    For example, in case gstomxh264dec, chain() function is defined on gstvideodecoder class, and it will let children’s class make specific handling via handle_frame() method.
    gstomxvideodec will implement for handle_frame() to make specific handling for OMX data.
    Besides, should care about event handling and query handling. It should be implement as _sink_event(), src_event(), sink_query() or src_query.

## Slide 43: Important points when reading source code of GStreamer
Comment:
  GStreamer framework only provide mechanism for transfer data, to handle for data must have specific knowledge of that data
For example, to understand gst-omx, must have knowledge of OMX; to understand v4l2src and vspfilter, must have knowledge of v4l2 framework; to understand waylandsink, must have knowledge of wayland/Weston.

## Slide 44: How to debug
GStreamer provide many level for debugging, can enable it by export GST_DEBUG=# (#=0,1, ..8)
# | Name | Description
0 | none | No debug information is output.
1 | ERROR | Logs all fatal errors.
2 | WARNING | Logs all warnings.
3 | FIXME | Logs all "fixme" messages
4 | INFO | Logs all informational messages.
5 | DEBUG | Logs all debug messages.
6 | LOG | Logs all log messages.
7 | TRACE | Logs all trace messages.
8 | MEMDUMP | Logs all memory dump messages.

## Slide 45: How to debug
Or can enable debug by using --gst-debug=# in gst-launch
  Ex:
gst-launch-1.0 filesrc location=file.mp4 ! qtdemux ! h264parse ! omxh264dec ! vspfilter ! waylandsink --gst-debug=2
Can debug base on name of element
  Ex:
  gst-launch-1.0 filesrc location=file.mp4 ! qtdemux ! h264parse ! omxh264dec ! vspfilter ! waylandsink --gst-debug=*omx*:9
  => It will show all debug log of gst-omx packages (gstomxh264dec, gstomxvideodec, gstomx,…)

## Slide 46: Reference
For more information please refer to following link:
  https://gstreamer.freedesktop.org/documentation/application-development/index.html
  https://gstreamer.freedesktop.org/documentation/plugin-development/index.html
  https://gstreamer.freedesktop.org/documentation/plugins.html

## Slide 47
Renesas.com

## Slide 48: Appendix – reference for making pipeline
General order of GST pipeline with Video and Audio
# gst-launch-1.0 filesrc location=file.extension ! demuxer name=d d. ! queue ! video_parser ! video_decoder ! video_filter ! video_converter ! waylandsink d. ! queue ! audio_parser ! audio_decoder ! audio_filter ! audio_converter ! alsasink device=hw:0,0
Note: Filter (vspfilter, audioresample, etc.) and Converter (videoconvert, audioconvert, etc.) are optional.
Rule: choose demuxer follows extension; choose decoder follows standard
Similar for pipeline for Video or Audio only:
# gst-launch-1.0 filesrc location=file.extension ! demuxer ! video_parser ! video_decoder ! waylandsink
# gst-launch-1.0 filesrc location=file.extension ! demuxer ! audio_parser ! audio_decoder ! alsasink device=hw:0,0
extension | Video parser - decoder | Audio parser - decoder
qtdemux : mp4,3gp,mov,m4a matroskademux : mkv,webm tsdemux : trp, ts asfdemux : wmv, wma avidemux : avi | H264 : h264parse - omxh264dec H265 : h265parse -omxh265dec MPEG4 : mpeg4videoparse - omxmpeg4videodec VC-1 : none - omxvp8dec VP8 : none - omxvc1dec | AAC : aacparse - omxaacdec MP3 : mpegaudioparse - omxmp3dec WMA : none - omxwmadec VORBIS : none - vorbisdec